## Slide 1: Why people Hate public Transportation ?

## Slide 2: What’s the Problem?
Sri Lanka has the second highest road density in Asia (173.8 km/km2)
Once CTB was the largest omnibus company in the world (Wikipedia)
But Still people don’t use the public transportation very much

## Slide 3: Our Solution
Safer Travel Utility

## Slide 4
Web App
Tracker
Mobile App
What You See from Outside

## Slide 5
Web App api
Mobile App api
Google API Services
Application DB
TMS
Tracker
Tracker
Tracker
Tracker
Tracker
Service API

## Slide 6
What You Don’t See from Outside
MQTT Broker
Tracker 1
Tracker 2
Tracker 3
TMS Backend
TMS DB
TMS Web Console
S
E
R
V
I
C
E
A
P
I

## Slide 7: Why MQTT
Light weight
Flexible
Secure
Scalable
Low bandwidth

## Slide 8
What’s Inside the Tracker
GPS + GSM Module
(A9G chip)
IMU Module
(MPU 6050)
Magnetometer
(hmc5883l)
Barometric Pressure Sensor
(BMP 280)
Battery Lion 3.7v
12v to 3.7v SMPS Module
DC Input
Microcontroller
(STM32F103)
Power bus
Data bus

## Slide 9
S
E
R
V
I
C
E
A
P
I
Web App API
Mobile App API
Google API Services
Application DB

## Slide 12
SaVy

## Slide 13
Bill Of Materials Per Unit
Item | No Of Units | Price/Unit | cost
MPU 6050 | 1 | 390 | 390
BMP 280 | 1 | 330 | 330
HMC 5983 | 1 | 750 | 750
A9G | 1 | 3000 | 3000
STM32F103C8T6 | 1 | 750 | 750
LM2596 Adjustable Buck Converter | 1 | 180 | 180
Li Ion Battery | 1 | 220 | 220
Enclosure Box | 1 | 290 | 290
Total |  |  | 5910

## Slide 14
week3
Mobile APP
WEB UI
TMS
Tracker
2015
2018
YOUR HEADING
YOUR HEADING
YOUR HEADIG
TIMELINE
Week7
Week11
Final

## Slide 15
How we going to demonstrate